## Slide 1
Presented by
Frank Larkin – FRC272
Lansdale Catholic Robotics
FIRST Boot Camp Seminar – Dec. 11, 2016

## Slide 2
In the FIRST competition an awesome robot will…
  Either use CarbonBU or SiliconBU sensors
  Help driver or operator by having several automated systems in place to handle competition work load.
  Most Importantly: Provide good visual feedback to tell operator what is happening. Preferably heads up.

## Slide 3
What is a sensor?
  A device that detects and communicates some aspect of your environment
  You process it so it makes sense in your context.
  You then understand hat it means.
  Then you do something with information
Human sequence…
Detect: Eyes see light in front of you, tells Brain
Process: Brain sees a familiar shape. Oh it’s Mark from 3rd period physics
Understand: Brain reminds you that you promised to go to Prom with him but you are just accepted invite from Jim!!!!!!!
Action: Brain tells you not to make eye contact, look down and walk, do not run, away quickly but gracefully.

## Slide 4
Multiple choices to mix and match
  Axis Camera
    2 dimensional - can give you weight, size and X and Y for target location.
    Can be slow as roboRIO cycles are used to determine target.
  Infra red (IR) Proximity sensors
    Can be purchased to cover various distances
    Detects reflected light, broad or narrow beam, inexpensive
  Ultra-Sonic Range finders
    Can be purchased with various beam widths.
    Can interfere with each other.
  Encoders
    Turn rotation into position control or distance covered, come in many flavors
Many vendors
      www.robotshop.com www.andymark.com
      www.acroname.com www.sparkfun.com

## Slide 5
LC 2007 Tube Detector (C++)
  Press button to arm automation
  Drive into pile of tubes
  IR Sensor detected presence of close Tube.
  Automation engaged Claw to capture Tube
  Driver station showed red when close, green on capture
LC 2010 Ball Detector (C++)
  Press and hold button starts automation. Robot moves forward
  Left / Right IR Sensors detected object and Steered Robot to object
  Switch in suction cup detected Ball contact
    Triggered robot to back up (visual feedback)

## Slide 6
LC 2011 Tube Tower (C++)
  Robot knew how high the tower was and adjusted automatically. I button for each height
  Autonomous mode “knew” how far it was from the wall to know when to drop tube.
LC 2015 Processes (Java/Robot Builder)
  Tower knew its position. Several stop points for automation
  Wedge knew its position. Several pre-programmed stop points.
  IR and Banner sensors detected totes for blended operation.

## Slide 7
All switch sensors plug into the digital-in, analog to analog
  White – Signal (SIG, S)
  Red – Center 5 volt power to power device. (not usually needed for switches) (PWR, 5V)
  Black – Ground (GND)
  Some devices need more power, connect power (red & black) to power panel, white to Digital In
Digital (on/off) Analog (range in voltage)

## Slide 8
All switches have effectively 2 positions on or off
Switches have a normal state and an activated state
  There are usually connectors for normally open (no) or normally closed (nc).
  Switch usually allows you to select the state depending where you connect the wires.
  Which is better?
    NO is easier to understand. Press switch make contact. If wire broken switch is useless.
    NC means when Not Pressed you have a circuit. When pressed the circuit opens. If you boot up robot and switch appears activated, you may have a broken wire.
NC
NO
CO
Normal State
NC
NO
CO
Active State
Digital White wire (signal)
Digital Black wire
Outside force
presses down

## Slide 9
Have emitter and detector in same package
  Usually have sensitivity control
Use retro reflective tape placed on opposite side of target. Target breaks beam.
Will usually have 4 wires
  Blue – 10 – 30 volt power. Connects to the circuit breaker panel. Yes you need a circuit breaker!!!!!
  Brown – Ground
  White – NO (normally open) switch position
  Black – NC (normally closed) switch position
You need to solder the wires from the sensor to the correct wires on the switch. Test without soldering first to ensure you are correct.
Favorite: www.bannerengineering.com

## Slide 10
Sharp Infrared IR GP2Y0A21YK0F sensor
  Range – 10cm – 80cm 4 inches to 30 inches
  Cost < $15
  Interface
    Directly connected to analog bumper.
    Returns a number from 1 (far away) to 512 (close up)
    Dead zone from 4” – 0”
      If detecting very close objects, recess into robot frame.
  Important: Make sure you purchase wired connector. Saves a lot of headaches.
  roboRio digital 5 volt power will power this device.

## Slide 11
Sharp Infrared IR GP2Y0A21YK0F sensor
  Transmitter / Receiver in the same package
  Response show how device operates
  Why the drop as we get close?
  How can we manage that?

## Slide 12
Connected to analog-in on analog bumper
  Black= Ground
  Red = 5 volt power
  White – Signal
You must connect to proper connections on sensor.

## Slide 13
Activate process
  Driver gets to within 3 feet of ball
  Holds joystick button to activate
  Process takes over controls
  Robot rolls forward
  Operator still has X and Y to “help”
Two IR sensors on either side of suction cup
  Spaced ~ a ball width apart.
  Low value (1-10) indicates nothing in front.
  High value indicates ball is there.
  Slide to the side where the ball is.
  How do you use the numbers you get?
    Subtract numbers. If difference > 50 we have an object.
    Negative = move left, positive = move right.
Contact switch in suction cup
  Indicates we have capture
  Process back up as long as button is pressed
Click image to play video
From LC website

## Slide 14
Problem
  How to create automated tower operation?
  String Potentiometer
    Tower goes up pulls out sting
    that turns a barrel
    that turns a shaft
    that turns a potentiometer
    that sends us a number
    that we map to height
  Robot knows how high or low it is.

## Slide 15
Solution
  Operator tells tower to go to floor
  When tower below certain point “wrist” drops
  When down “finger” drops
  Completely automatic
  Capture:
    Operator pulls and holds trigger
    Software runs autonomous process
    Picks up finger
    Raises tower
    Picks up wrist
    Raises to hold position
  Positioning
    Operator presses and hold button
    Tower goes to that position

## Slide 16
Store joystick inputs in variables
  Create separate variables to hold what joystick position and buttons are calling for. True “Fly by Wire”. Example: Joystick X, Y and buttons are stored in variables
Decide what to do before setting outputs
  Use function to decide if what to do based upon sensors. Example: If we are in deploy mode (button pressed)…
    Banner sensor tells you a tot is there. Push off only 1.
    No tote push the back one
Set Outputs
  Set outputs based upon variables that may have been cooked by other code.

## Slide 18
Day 1 – What do we need to automate?
  How can we make the driver’s job easier?
Purchase sensors early
  Many teams know the secrets
  Get hold of sensors. They are cheap.
  Experiment
  Challenge yourself
Look at old code
  LC 2010 code http://www.frc272.com/seminar/Archive/LC2010_robot_code.zip
  LC 2011 code http://www.frc272.com/seminar/Archive/LC2011_robot_code.zip
    Questions – pafwl@aol.com